## Slide 1
Layout Strategies
9

## Slide 2: Strategic Importance of Layout Decisions
Develop an effective and efficient layout that will meet the firm’s competitive requirements

## Slide 3: Layout Design Considerations
Higher utilization of space, equipment, and people
Improved flow of information, materials, or people
Improved employee morale and safer working conditions
Improved customer/client interaction
Flexibility

## Slide 4: Good Layouts Consider
Material handling equipment
Capacity and space requirements
Environment and aesthetics
Flows of information
Cost of moving between various work areas

## Slide 5: Layouts Enhancements
Ambient conditions
  Background characteristics such as lighting, sound, smell, and temperature
Spatial layout and functionality
  Customer circulation path planning, aisle characteristics, and product grouping
Signs, symbols, and artifacts
  Characteristics of building design that carry social significance

## Slide 6: Types of Layout
Office layout
Retail layout
Warehouse layout
Fixed-position layout
Process-oriented layout
Work-cell layout
Product-oriented layout

## Slide 7: Real Examples
TABLE 9.1 | Layout Strategies |  | 
 |  | OBJECTIVES | EXAMPLES
Office |  | Locate workers requiring frequent contact close to one another | EB Depts – Where locate? NER – Open offices
Retail |  | Expose customer to high-margin items | 
Warehouse (storage) |  | Balance low-cost storage with low-cost material handling | Chem Safety – Reg issues MLS – Limited storage
Project (fixed position) |  | Move material to the limited storage areas around the site | Electric Boat – Sub construction
Job Shop (process oriented) |  | Manage varied material flow for each product | EB QP – Assembly areas Fender – Guitars
Work Cell (product families) |  | Identify a product family, build teams, cross-train team members | F&O – Separate by reg type Food Prod – Allergens
Repetitive/ Continuous (product oriented) |  | Equalize the task time at each workstation | Gorton’s – Production line Colfor – Production area NECCO – ? Min handling

## Slide 8: Office – Open Desks

## Slide 9: Office – Traditional Cubicle

## Slide 10: Office – Modern Cubicle

## Slide 11: Relationship Chart
Figure 9.1

## Slide 12: Relationship Diagramming Example – Survey Results
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable
Area | Code
Production to Offices | O
Production to Stockroom | A
Production to Ship&Rece | I
Production to Locker room | E
Production to Toolroom | A
Offices to Stockroom | U
Offices to Ship&Rece | O
Area | Code
Offices to Locker room | X
Offices to Toolroom | U
Stockroom to Ship&Rece | A
Stockroom to Locker room | U
Stockroom to Toolroom | O
Ship&Rece to Locker room | U
Ship&Rece to Toolroom | O
Locker room to Toolroom | O

## Slide 13: Relationship Diagramming Example
Production
Offices
Stockroom
Shipping and receiving
Locker room
Toolroom
How important is having the locker room and offices adjacent to each other?
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable
Area | Code
Offices to Locker room | X

## Slide 14: Relationship Diagramming Example
Production
Offices
Stockroom
Shipping and receiving
Locker room
Toolroom
X
How important is having the locker room and offices adjacent to each other?
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable
Area | Code
Offices to Locker room | X

## Slide 15: Relationship Diagramming Example
Production
Offices
Stockroom
Shipping and receiving
Locker room
Toolroom
How important is having the stockroom and toolroom adjacent to each other?
X
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable
Area | Code
Stockroom to Toolroom | O

## Slide 16: Relationship Diagramming Example
Production
Offices
Stockroom
Shipping and receiving
Locker room
Toolroom
X
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable
A
O
U
X
I
E
A
O
U
X
I
E
A
O
U
X
I
E
A
O
U
X
I
E
A
O
U
X
I
E

## Slide 17: Relationship Diagramming Example
A
A
A
O
O
O
O
O
U
U
U
U
E
X
I
Production
Offices
Stockroom
Shipping and receiving
Locker room
Toolroom
A - Absolutely necessary
E - Especially important
I - Important
O - Okay
U - Unimportant
X - Undesirable

## Slide 18: Retail Layout
Objective is to maximize profitability per square foot of floor space
Sales and profitability vary directly with customer exposure

## Slide 19: Store Layout
Figure 9.2

## Slide 20: Warehouse and Storage Layouts
Objective
  Find the optimum trade-offs between handling costs and costs associated with warehouse space
Maximize the total “cube” of the warehouse
  Use its full volume while maintaining low material handling costs

## Slide 21: Cross-Docking
Materials are moved directly from receiving to shipping and are not placed in storage in the warehouse
Requires tight scheduling and accurate shipments, bar code or RFID identification used for advanced shipment notification as materials are unloaded

## Slide 22: Fixed-Position Layout
Product remains in one place
  Materials come to it
    Extreme example is a house
Workers and equipment come to site
Complicating factors
  Limited space at site
  Different materials required at different stages of the project
  Volume of materials needed is dynamic

## Slide 23: Fixed Position Example

## Slide 24: Process-Oriented Layout
Like machines and equipment are grouped together
Flexible and capable of handling a wide variety of products or services
Scheduling can be difficult and setup, material handling, and labor costs can be high

## Slide 25: Process Layout

## Slide 26: Process Layout Calculation
where n = total number of work centers or departments
i, j = individual departments
Xij = number of loads moved from department i to department j
Cij = cost to move a load between department i and department j

## Slide 27: Process Layout Example
Room 1 Room 2 Room 3
Room 4 Room 5 Room 6
60'
40'
Receiving Shipping Testing
Department Department Department
(4) (5) (6)
Figure 9.5
Assembly Painting Machine Shop
Department Department Department
(1) (2) (3)
Assume: 20 feet between center of each room

## Slide 28: Process Layout Example
Answer the following questions for a 60 by 40 foot facility divided into 6 equal sections with the loads per week movement charts below. Assume the cost for each move is 3 dollars. Traffic never flows diagonally.
  What is the optimal arrangement of rooms?
  What is the expected cost?

## Slide 29: Process Layout – Revised
Room 1 Room 2 Room 3
Room 4 Room 5 Room 6
Painting Receiving Shipping
Department Department Department
Assembly Machine Shop Testing
Department Department Department
Total movement = 11,460
Total cost = $34,380

## Slide 30: Work Cells
Reorganizes people and machines into groups to focus on single products or product groups
Group technology identifies products that have similar characteristics for particular cells
Volume must justify cells
Cells can be reconfigured as designs or volume changes

## Slide 31: Improving Layouts Using Work Cells
Current layout - workers in small closed areas.
Improved layout - cross-trained workers can assist each other. May be able to add a third worker as additional output is needed.
Figure 9.9 (a)
Material

## Slide 32: Improving Layouts Using Work Cells
Current layout - straight lines make it hard to balance tasks because work may not be divided evenly
Improved layout - in U shape, workers have better access. Four cross-trained workers were reduced to three.
Figure 9.9 (b)
U-shaped line may reduce employee movement and space requirements while enhancing communication, reducing the number of workers, and facilitating inspection

## Slide 33: 5 Potential Work Cell Advantages
Grouped tasks leads to more frequent inspections
Fewer workers are needed
Workers can reach more of the work area
Work area can be more efficiently balanced
Communication is generally better

## Slide 34: Staffing and Balancing Work Cells
Determine the number of operators required
Workers required =
Total operation time required
Takt time
Determine the Takt time
Takt time =
Total work time available
Units required to satisfy customer demand

## Slide 35: Staffing Work Cells Example
600 mirrors per day required
Mirror production scheduled for 8 hours per day
From a work balance chart total operation time = 140 seconds
Standard time required
Operations
Assemble
Paint
Test
Label
Pack for
shipment
60
50
40
30
20
10
0
Figure 9.10

## Slide 36: Staffing Work Cells Example
600 mirrors per day required
Mirror production scheduled for 8 hours per day
From a work balance chart operation time = 140 seconds
Takt time = Pace of production to meet customer demands
Takt time = (8 hrs x 60 mins) / 600 units
= 0.8 min = 48 seconds
Workers required =
Total operation time required
Takt time
= 140 / 48 = 2.9
= 3

## Slide 37: Product-Oriented Layout
Volume is adequate for high equipment utilization
Product demand is stable enough to justify high investment in specialized equipment
Product is standardized or approaching a phase of life cycle that justifies investment
Supplies of raw materials and components are adequate and of uniform quality
Organized around products or families of similar high-volume, low-variety products

## Slide 38: Product-Oriented Layouts
Advantages
  Low variable cost per unit
  Low material handling costs
  Reduced work-in-process inventories
  Easier training and supervision
  Rapid throughput
Disadvantages
  High volume is required
  Work stoppage at any point ties up the whole operation
  Lack of flexibility in product or production rates

## Slide 39: McDonald's Assembly Line
Figure 9.11

## Slide 40: Assembly-Line Balancing
Objective is to minimize the imbalance between machines or personnel while meeting required output
  Starts with the precedence relationships
  Determine cycle time
  Calculate theoretical minimum number of workstations
  Balance the line by assigning specific tasks to workstations

## Slide 41: Cycle Time – Cd
Cd =
production time available
desired units of output
Cd =
(8 hours x 60 minutes / hour)
(120 units)
Cd = = 4 minutes
480
120
Variable | Data
Production Time | 8 hours (480 minutes)
Desired Output | 120 units

## Slide 42: Flow Time vs Cycle Time
Cycle time = max time spent at any station
1
2
3
7 minutes
3 minutes
5 minutes
Cycle time = max (7, 3, 5) = 7 minutes

## Slide 43: Line Balancing Process
1. Draw and label a precedence diagram
2. Calculate the desired cycle time required for the line
3. Calculate the theoretical minimum number of workstations
4. Group elements into workstations, recognizing cycle time and precedence constraints
5. Calculate the efficiency of the line
6. Stop if…
  Theoretical minimum number of workstations
  OR
  Acceptable efficiency level reached
    If not, go back to step 4

## Slide 44: Wing Component Example
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | TASK MUST FOLLOW TASK LISTED BELOW
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
480 available mins per day
40 units required

## Slide 45: Wing Component Example
TABLE 9.2 |  | Precedence Data for Wing Component |  |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | TASK MUST FOLLOW TASK LISTED BELOW: PREDECESSOR | 
A |  |  | 10 |  | – | 
B |  |  | 11 |  | A | 
C |  |  | 5 |  | B | 
D |  |  | 4 |  | B | 
E |  |  | 11 |  | A | 
F |  |  | 3 |  | C, D | 
G |  |  | 7 |  | F | 
H |  |  | 11 |  | E | 
I |  |  | 3 |  | G, H | 
Total time |  |  | 65 |  |  | 
This means that tasks B and E cannot be done until task A has been completed

## Slide 46: Complete the Diagram
I
3
G
7
F
3
C
5
D
4
H
11
B
11
E
11
A
10
TABLE 9.2 |  | Precedence Data |  |  | 
TASK | TIME (MINUTES) |  |  |  | Predecessor
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H

## Slide 47: Wing Component Example
I
G
F
C
D
H
B
E
A
10
11
11
5
4
3
7
11
3
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PEDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Figure 9.12

## Slide 48: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
Minimum number of workstations

## Slide 49: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day

## Slide 50: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40

## Slide 51: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40
= 12 minutes per unit

## Slide 52: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40
= 12 minutes per unit
Minimum number of workstations

## Slide 53: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40
= 12 minutes per unit
Minimum number of workstations
= 65 / 12

## Slide 54: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40
= 12 minutes per unit
Minimum number of workstations
= 65 / 12
= 5.4

## Slide 55: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time =
Production time available per day
Units required per day
= 480 / 40
= 12 minutes per unit
Minimum number of workstations
= 65 / 12
= 5.4
= 6 stations

## Slide 56: Rules for Assigning Workstations
TABLE 9.3 | Layout Heuristics That May Be Used to Assign Tasks to Workstations in Assembly-Line Balancing | 
1. Longest task time |  | From the available tasks, choose the task with the largest (longest) task time
2. Most following tasks |  | From the available tasks, choose the task with the largest number of following tasks
3. Ranked positional weight |  | From the available tasks, choose the task for which the sum of following task times is the longest
4. Shortest task time |  | From the available tasks, choose the task with the shortest task time
5. Least number of following tasks |  | From the available tasks, choose the task with the least number of subsequent tasks

## Slide 57: Assign the Workstations
Station 1
Station 2
Station 3
Station 4
Station 3
Station 5
Station 6
Station 6
I
G
F
H
C
D
B
E
A
10
11
11
5
4
3
7
11
3
480 available mins per day
40 units required
Cycle time = 12 mins
Minimum workstations
= 6

## Slide 58: Wing Component Example
Station 1
Station 2
Station 3
Station 5
Station 3
Station 4
Station 6
Station 6
I
G
F
H
C
D
B
E
A
10
11
11
5
4
3
7
11
3
480 available mins per day
40 units required
Cycle time = 12 mins
Minimum workstations
= 6

## Slide 59: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency =
∑ Task times
(Actual number of workstations) x (Largest cycle time)

## Slide 60: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency =
∑ Task times
(Actual number of workstations) x (Largest cycle time)
= 65 minutes

## Slide 61: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency =
∑ Task times
(Actual number of workstations) x (Largest cycle time)
= 65 minutes / ((6 stations)

## Slide 62: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency =
∑ Task times
(Actual number of workstations) x (Largest cycle time)
= 65 minutes / ((6 stations) x (12 minutes))

## Slide 63: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency =
∑ Task times
(Actual number of workstations) x (Largest cycle time)
= 65 minutes / ((6 stations) x (12 minutes))
= 90%

## Slide 64: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Idle Time =
(Actual number of workstations x Largest assigned cycle time) - ∑ Task times
Efficiency:
90%

## Slide 65: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Idle Time = ((6 stations) × (12 minutes)) – 65 minutes
= 72 - ∑ Task times
Efficiency:
90%

## Slide 66: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Idle Time = ((6 stations) × (12 minutes)) – 65 minutes
= 72 - ∑ Task times
= 7 minutes
Efficiency:
90%

## Slide 67: Wing Component Example
480 available mins per day
40 units required
TABLE 9.2 |  | Precedence Data for Wing Component |  |  | 
TASK | ASSEMBLY TIME (MINUTES) |  |  |  | PREDECESSOR
A |  |  | 10 |  | –
B |  |  | 11 |  | A
C |  |  | 5 |  | B
D |  |  | 4 |  | B
E |  |  | 11 |  | A
F |  |  | 3 |  | C, D
G |  |  | 7 |  | F
H |  |  | 11 |  | E
I |  |  | 3 |  | G, H
Total time |  |  | 65 |  | 
Cycle time:
12 minutes per unit
Min workstations:
6 stations
Efficiency:
90%
Idle Time:
7 minutes

## Slide 68: Sample HW Problem

## Slide 69: Sample HW Problem – Solution

## Slide 70: Self Assessment
Draw a rough diagram of the layout of your favorite store
  Using the ideas from this class, discuss good and bad layout strategies
Consider a warehouse for a company selling computers and computer supplies (Staples or Office Depot)
  How would you organize this warehouse to optimize the layout?

## Slide 71: Supplemental

## Slide 72: Layouts
A company hired your operations management consulting firm to improve the layouts of their offices, store, and warehouse.
  How would you do this and what general Operations Management fundamentals should be considered?

## Slide 73: Office Layout
Grouping of workers, their equipment, and spaces
  Provide comfort, safety, and movement of information
  Movement of information is main distinction
  Can change due to technological changes
    Cubicles vs. Open desks

## Slide 74: Office Layout
Physical, political, and social aspects
  Proximity
  Privacy
  Seniority
Two major trends
  Information technology
  Dynamic needs for space and services

## Slide 75: 5 Ideas for Supermarket Layout
Locate high-draw items around the periphery of the store
Use prominent locations for high-impulse and high-margin items
Distribute power items to both sides of an aisle and disperse them to increase viewing of other items
Use end-aisle locations
Convey mission of store through careful positioning of lead-off department

## Slide 76: Warehouse and Storage Layouts
Material Handling Costs
All costs associated with the transaction
  Incoming transport
  Storage
  Finding and moving material
  Outgoing transport
  Equipment, people, material, supervision, insurance, depreciation
Minimize damage and spoilage

## Slide 77: Warehouse and Storage Layouts
Warehouse density tends to vary inversely with the number of different items stored
Automated Storage and Retrieval Systems (ASRSs) can significantly improve warehouse productivity
Dock location is a key design element
  One way in
  One way out

## Slide 78: Process-Oriented Layout
Arrange work centers so as to minimize the costs of material handling
Basic cost elements are
  Number of loads (or people) moving between centers
  Distance loads (or people) move between centers

## Slide 79: Process-Oriented Layout
Surgery
Radiology
ER triage room
ER Beds
Pharmacy
Emergency room admissions
Billing/exit
Laboratories
Patient A - broken leg
Patient B - erratic heart pacemaker
Figure 9.3