## Slide 1
Lean Operations
16

## Slide 2: Lean Operations
Supply the customer with exactly what the customer wants when the customer wants it, without waste, through continuous improvement
Driven by “pulling” customer orders

## Slide 3: Reduce Variability
Inventory level
Process downtime
Scrap
Setup time
Late deliveries
Quality problems
Figure 16.3

## Slide 4: Reduce Variability
Inventory level
Figure 16.3
Process downtime
Scrap
Setup time
Late deliveries
Quality problems

## Slide 5: Reduce Variability
Inventory level
Figure 16.3
Process downtime removed
No scrap
Setup time reduced
No late deliveries
Quality problems removed

## Slide 6: Ohno's Seven Wastes
Overproduction
Queues
Transportation
Inventory
Motion
Overprocessing
Defective products

## Slide 7: The 5Ss
Sort/segregate – when in doubt, throw it out
Simplify/straighten – methods analysis tools
Shine/sweep – clean daily
Standardize – remove variations from processes
Sustain/self-discipline – review work and recognize progress
Not part of the 5 Ss
  Safety – built in good practices
  Support/maintenance – reduce variability and unplanned downtime

## Slide 8: 5S Charts

## Slide 9: 5S Example
Sort/segregate
Simplify/straighten
Shine/sweep
Standardize
Sustain/self-discipline

## Slide 10: Lean Operations
Just-in-time (JIT) focuses on continuous forced problem solving
Toyota Production System (TPS) emphasizes continuous improvement, respect for people, and standard work practices in an assembly-line environment

## Slide 11: Lean Operations
Encompasses JIT, TPS, Kanban…
Sustains competitive advantage and increases return to stakeholders
Three fundamental issues
  Eliminate waste
  Remove variability
  Improve throughput

## Slide 12: Lean and Just-In-Time
Powerful strategy for improving operations
Materials arrive where they are needed only when they are needed
Identifying problems and driving out waste reduces costs and variability and improves throughput
Requires a meaningful buyer-supplier relationship

## Slide 13: Supplier Partnerships
Exist when a supplier and purchaser work together to remove waste and drive down costs
Four goals of supplier partnerships are:
  Removal of unnecessary activities
  Removal of in-plant inventory
  Removal of in-transit inventory
  Improved quality and reliability

## Slide 14: Concerns of Suppliers
Need
  Collaboration, Mutual understanding, and Trust
Diversification
  Ties to only one customer increases risk
Scheduling
  Don't believe customers can create a smooth schedule
Lead time
  Short lead times mean engineering or specification changes can create problems
Quality
  Limited by capital budgets, processes, or technology
Lot sizes
  Small lot sizes may transfer costs to suppliers

## Slide 15: Lean Scheduling
Better scheduling improves performance
TABLE 16.3 | 
LEAN SCHEDULING TACTICS | 
Make level schedules | 
Use kanbans | 
Communicate schedules to suppliers | 
Freeze part of the schedule | 
Perform to schedule | 
Seek one-piece-make and one-piece-move | 
Eliminate waste | 
Produce in small lots | 
Make each operation produce a perfect part | 

## Slide 16: Lean Layout
Reduce waste due to movement
TABLE 16.1 | 
LEAN LAYOUT TACTICS | 
Build work cells for families of products | 
Include a large number operations in a small area | 
Minimize distance | 
Design little space for inventory | 
Improve employee communication | 
Use poka-yoke devices | 
Build flexible or movable equipment | 
Cross-train workers to add flexibility | 

## Slide 17: Lean Inventory
Inventory is at the minimum level necessary to keep operations running
TABLE 16.2 | 
LEAN INVENTORY TACTICS | 
Use a pull system to move inventory | 
Reduce lot sizes | 
Develop just-in-time delivery systems with suppliers | 
Deliver directly to point of use | 
Perform to schedule | 
Reduce setup time | 
Use group technology | 

## Slide 18: Reduce Lot Sizes
Ideal situation is to have lot sizes of one pulled from one process to the next
Often not feasible
Can use EOQ analysis to calculate desired setup time
Two key changes necessary
  Improve material handling
  Reduce setup time

## Slide 19: Setup Time Example
D = Annual demand = 400,000 units
d = Daily demand = 400,000/250 = 1,600 per day
p = Daily production rate = 4,000 units
Qp = EOQ desired = 400 units
H = Holding cost = $20 per unit
S = Setup cost (to be determined)
R = Hourly rate for setup personnel = $30
Setup time = $2.40/($30/hour) = 0.08 hr = 4.8 minutes

## Slide 20: Reduce Setup Costs
High setup costs encourage large lot sizes
Reducing setup costs reduces lot size and reduces average inventory
Setup time can be reduced
  Preparation prior to shutdown
  Changeover

## Slide 21: Lean Scheduling
Schedules must be communicated inside and outside the organization
Level schedules
  Process frequent small batches
  Freezing the schedule helps stability
Kanban
  Signals used in a pull system

## Slide 22: Kanban
Japanese word for card
The card is an authorization for the next container of material to be produced
A sequence of kanbans pulls material through the process
Many different sorts of signals are used, but the system is still called a kanban

## Slide 23: Kanban
When there is visual contact
  The user removes a standard-size container of parts from a small storage area, as shown in Figure 16.8.
  The signal at the storage area is seen by the producing department as authorization to replenish the using department or storage area. Because there is an optimum lot size, the producing department may make several containers at a time.

## Slide 24: Kanban
Signal marker hanging on post for part Z405 shows that production should start for that part. The post is located so that workers in normal locations can easily see it.
Signal marker on stack of boxes
Part numbers mark location of specific part
Figure 16.8

## Slide 25: Kanban
When the producer and user are not in visual contact, a card can be used; otherwise, a light or flag or empty spot on the floor may be adequate
Usually each card controls a specific quantity of parts although multiple card systems may be used if there are several components or if the lot size is different from the move size

## Slide 26: Kanban
Information Flow
Kanban
Kanban
Final assembly
Work cell
Kanban
Material/Parts Supplier
Finished goods
Customer order
 END ------------------------------ Pull System ------------------------------ START 
Product Flow
 START ------------------------------ Pull System ------------------------------ END 

## Slide 27: The Number of Kanban Cards or Containers
Need to know the lead time needed to produce a container of parts
Need to know the amount of safety stock needed
Number of kanbans
(containers)
Demand during Safety lead time + stock
Size of container
=

## Slide 28: Number of Kanbans Example
Daily demand = 500 cakes
Production lead time = 2 days
(Wait time +
Material handling time +
Processing time)
Safety stock = 1/2 day
Container size = 250 cakes
Demand during lead time = 2 days x 500 cakes = 1,000
Safety stock = ½ x Daily demand = 250
Number of kanbans = = 5
1,000 + 250
250

## Slide 29: Advantages of Kanban
Small containers require tight schedules, smooth operations, little variability
Shortages create an immediate impact
Places emphasis on meeting schedules, reducing lead time and setups, and economic material handling
Standardized containers reduce weight, disposal costs, wasted space, and labor

## Slide 30: Lean Quality
Strong relationship
  Lean cuts the cost of obtaining good quality because Lean exposes poor quality
  Because lead times are shorter, quality problems are exposed sooner
  Better quality means fewer buffers and allows simpler Lean systems to be used

## Slide 31: Lean Quality Tactics
TABLE 16.4 | 
LEAN QUALITY TACTICS | 
Use statistical process control | 
Empower employees | 
Build fail-safe methods (poka-yoke, checklists, etc.) | 
Expose poor quality with small lots | 
Provide immediate feedback | 

## Slide 32: Toyota Production System
Continuous improvement
  Build an organizational culture and value system that stresses improvement of all processes, kaizen
  Part of everyone’s job
Respect for people
  People are treated as knowledge workers
  Engage mental and physical capabilities
  Empower employees
“Not my job” = Never
  Stopping production because of a defect is called jidoka

## Slide 33: Toyota Motor Corporation
Success due to two techniques, JIT and TPS
Continual problem solving is central to JIT
Eliminating excess inventory makes problems immediately evident
Central to TPS is employee learning and a continuing effort to produce products under ideal conditions
Respect for people is fundamental
Small building but high levels of production
Subassemblies are transferred to the assembly line on a JIT basis
High quality and low assembly time per vehicle

## Slide 34: TPS Elements
https://www.youtube.com/watch?v=cAUXHJBB5CM

## Slide 35: Lean Organizations
Understanding the customer and their expectations
Functional areas communicate and collaborate to make sure customer expectations are met
Implement the tools of Lean throughout the organization

## Slide 36: Building a Lean Organization
Transitioning to a Lean system can be difficult
Build a culture of continual improvement
Open communication
Demonstrated respect for people
Gemba walks to see work being performed
  Japanese term meaning "the real place"

## Slide 37: Building a Lean Organization
Lean systems tend to have the following attributes
  Respect and develop employees
  Empower employees
  Develop worker flexibility
  Develop collaborative partnerships with suppliers
  Eliminate waste by performing only value-added activities

## Slide 38: Lean in Services
The Lean techniques used in manufacturing are used in services
  Report generation
  Service time
  Staffing numbers

## Slide 39: Process Improvement
Lean is implemented through process improvement events
  Goal = investigate one business or technical process or function
  How = Many meetings
    Map out current issues
    Plan potential solutions
    Implement solutions
    Monitor progress
    Determine if further improvement needed