## Slide 1
Managing Quality
6

## Slide 2: Defining Quality
The totality of features and characteristics of a product or service that bears on its ability to satisfy stated or implied needs
  American Society for Quality

## Slide 3: Quality Perspective
Quality = Deliverable – Expectations
  Customer determines quality

## Slide 4: Defining Quality
An operations manager’s objective is to build a total quality management (TQM) system that identifies and satisfies customer needs

## Slide 5: Implications of Quality
Company reputation
  Perception of new products
  Employment practices
  Supplier relations
Product liability
  Reduce risk
Global implications
  Improved ability to compete

## Slide 6: Seven Concepts of TQM
Continuous improvement
Six Sigma
Taguchi concepts
Benchmarking
Employee empowerment
Just-in-time (JIT)
  Later in the semester
Knowledge of TQM tools

## Slide 7: TQM Tools
Tools for Generating Ideas
  Check Sheet
  Scatter Diagram
  Cause-and-Effect Diagram
Tools to Organize the Data
  Pareto Chart
  Flowchart (Process Diagram)
Tools for Identifying Problems
  Histogram
  Statistical Process Control Chart

## Slide 8: Seven Tools of TQM
(3) Cause-and-Effect Diagram: A tool that identifies process elements (causes) that may effect an outcome
  Also called Ishikawa or Fishbone diagrams
Figure 6.6
Cause
Materials
Methods
Manpower
Machinery
Effect
https://www.conceptdraw.com/samples/fishbone-diagram

## Slide 9: Layout

## Slide 10: Main Cause Categories
Manufacturing category examples
  Machines/Equipment
  Methods
  Materials
  People
Service category examples
  Policies
  Procedures
  Technical
  People

## Slide 11: Fishbone Problem
Late to class
Weather
Category
Category
Category
Category
Category
Snow
Cause
Cause
Cause
Cause
Cause
Cause
Cause
Cause
Cause
Cause
Cause

## Slide 12: Fishbone Problem
Late to class
Snow
Flat tire
Late leaving
Rain
Engine overheat
Poor planning
No reserved space
Cell phone died
Other activities
Special Event
Alarm failed
Previous class far
Weather
Schedule
Parking
Technical
Student
Vehicle

## Slide 13: Seven Tools of TQM
(4) Pareto Chart: A graph to identify and plot problems or defects in descending order of frequency
Figure 6.6
Frequency
Percent
A B C D E

## Slide 14: Pareto Charts
Number of occurrences
Room svc Check-in Pool hours Minibar Misc.
72% 16% 5% 4% 3%
12
4
3
2
54
– 100
– 93
– 88
– 72
70 –
60 –
50 –
40 –
30 –
20 –
10 –
0 –
Frequency (number)
Causes and percent of the total
Cumulative percent
Data for October

## Slide 15: Sample Pareto Chart

## Slide 16: Create a Pareto Chart

## Slide 17: Pareto Solution – ASQ Template
Chart: 
| Overpriced | Small portions | Wait time | Food is tasteless | No atmoshpere | Not clean | Too noisy | Food is too salty | Unfriendly staff | Food not fresh
 | 789 | 621 | 109 | 65 | 45 | 30 | 27 | 15 | 12 | 9
Percentage | 0.45819 | 0.81882 | 0.88211 | 0.91986 | 0.94599 | 0.96341 | 0.97909 | 0.9878 | 0.99477 | 1

## Slide 18: Pareto with Excel
Complaint | Count
Too noisy | 27
Overpriced | 789
Food is tasteless | 65
Food not fresh | 9
Food is too salty | 15
Not clean | 30
Unfriendly staff | 12
Wait time | 109
No atmoshpere | 45
Small portions | 621
1
2
3
4
5
6
For reference only. Use the ASQ Pareto template.

## Slide 19: Seven Tools of TQM
(7) Statistical Process Control Chart: A chart with time on the horizontal axis to plot values of a statistic
Figure 6.6
Upper control limit
Target value
Lower control limit
Time

## Slide 20: Statistical Process Control (SPC)
Variability is inherent in every process
  Natural causes
    Random
  Assignable causes
    Non-random
Provides a statistical signal when assignable causes are present
Detect and eliminate assignable causes of variation
Notes: Points which might be emphasized include:
- Statistical process control measures the performance of a process, it does not help to identify a particular specimen produced as being “good” or “bad,” in or out of tolerance.
- Statistical process control requires the collection and analysis of data - therefore it is not helpful when total production consists of a small number of units
- While statistical process control can not help identify a “good” or “bad” unit, it can enable one to decide whether or not to accept an entire production lot. If a sample of a production lot contains more than a specified number of defective items, statistical process control can give us a basis for rejecting the entire lot. The issue of rejecting a lot which was actually good can be raised here, but is probably better left to later.

## Slide 21: Variability
Random
  Caused by nature
    Weather
  Common causes
    Variation in material
  Inherent in a process
    Sampling protocol
  Can be eliminated only through improvements in the system
Non-Random
  Special causes
    Tampering
    New process
  Due to identifiable factors
    Change in personnel
    Part wear
  Can be modified through operator or management action

## Slide 22: Control Charts

## Slide 23: Control Charts
Constructed from historical data, the purpose of control charts is to help distinguish between natural variations and variations due to assignable causes
Notes: Students should understand both the concepts of natural and assignable variation, and the nature of the efforts required to deal with them.

## Slide 24: Control Chart Overview
17 = UCL
15 = LCL
16 = Mean
Sample number
| | | | | | | | | | | |
1 2 3 4 5 6 7 8 9 10 11 12
Control Chart for samples of 9 boxes
Variation due to assignable causes
Variation due to assignable causes
Variation due to natural causes
Out of control
Out of control
***For this class…use Excel to plot control charts

## Slide 25: A Process Is in Control If …
No sample points outside limits
Most points near process average
About equal number of points above and below centerline
Points appear randomly distributed

## Slide 26: Quality Measures
Variable
  Deliverable characteristic that is continuous and can be measured
  Falls within an acceptable range
  Weight; length
    Screen size, diameter of part
Attribute
  Deliverable characteristic that can be evaluated with a discrete response
  Does not address degree of failure
  Good or bad; yes or no
    Cell phone turns on, screen broken

## Slide 27: Control Chart Type
Variables
  Mean chart ( x -Chart )
    uses average of a sample
  Range chart ( R-Chart )
    uses amount of dispersion in a sample
Attributes
  p-charts
    Uses portion defective in a sample
  c-charts
    Uses number of defects in an item
Use different charts for each type

## Slide 28: Where to Use Control Charts
Process has a tendency to go out of control
Process is particularly harmful and costly if it goes out of control
Examples
  At the beginning of a process because it is a waste of time and money to begin production process with bad supplies
  Before a costly or irreversible point, after which product is difficult to rework or correct
  Before and after assembly or painting operations that might cover defects
  Before the outgoing final product or service is delivered

## Slide 29: Control Charts for Variable
Range & Mean

## Slide 30: Using X-Bar and R-Charts Together
Process average and process variability must be in control
It is possible for samples to have very narrow ranges, but their averages is beyond control limits
It is possible for sample averages to be in control, but ranges might be very large

## Slide 31: Mean and Range Charts
(a)
These sampling distributions result in the charts below
(Sampling mean is shifting upward, but range is consistent)
R-chart
(R-chart does not detect change in mean)
UCL
LCL
Figure S6.5
x-chart
(x-chart detects shift in central tendency)
UCL
LCL

## Slide 32: Mean and Range Charts
R-chart
(R-chart detects increase in dispersion)
UCL
LCL
(b)
These sampling distributions result in the charts below
(Sampling mean is constant, but dispersion is increasing)
x-chart
(x-chart indicates no change in central tendency)
UCL
LCL
Figure S6.5

## Slide 33: Restaurant Control Limits
For salmon filets at Darden Restaurants
Sample Mean
x Bar Chart
UCL = 11.524
= – 10.959
LCL = – 10.394
| | | | | | | | |
1 3 5 7 9 11 13 15 17
11.5 –
11.0 –
10.5 –
Sample Range
Range Chart
UCL = 0.6943
= 0.2125
LCL = 0
| | | | | | | | |
1 3 5 7 9 11 13 15 17
0.8 –
0.4 –
0.0 –

## Slide 34: Actual Control Chart Outputs

## Slide 35: Excel OM Use

## Slide 36: X-Bar and R-Chart Example
Number of samples | 10 | 
Sample size | 5 | 
Data |  | 
 | Mean | Range
Sample 1 | 22 | 2
Sample 2 | 24 | 3
Sample 3 | 21 | 5
Sample 4 | 19 | 2
Sample 5 | 22 | 3
Sample 6 | 20 | 7
Sample 7 | 21 | 2
Sample 8 | 22 | 1
Sample 9 | 22 | 2
Sample 10 | 24 | 3

## Slide 37: X-Bar and R-Chart Example
Quality control/x-bar chart |  | 
Number of samples | 10 | 
Sample size | 5 | 
Data |  | 
 | Mean | Range
Sample 1 | 4 | 2
Sample 2 | 4 | 3
Sample 3 | 6 | 1
Sample 4 | 7 | 3
Sample 5 | 3 | 1
Sample 6 | 6 | 3
Sample 7 | 3 | 2
Sample 8 | 5 | 1
Sample 9 | 8 | 5
Sample 10 | 2 | 1

## Slide 38: Control Charts for Attributes
p-Chart & c-Chart

## Slide 39: P-Chart
% Defective

## Slide 40: p-Chart for Data Entry
SAMPLE NUMBER | NUMBER OF ERRORS | FRACTION DEFECTIVE | SAMPLE NUMBER | NUMBER OF ERRORS |  |  | FRACTION DEFECTIVE
1 | 6 | .06 | 11 |  | 6 |  | .06
2 | 5 | .05 | 12 |  | 1 |  | .01
3 | 0 | .00 | 13 |  | 8 |  | .08
4 | 1 | .01 | 14 |  | 7 |  | .07
5 | 4 | .04 | 15 |  | 5 |  | .05
6 | 2 | .02 | 16 |  | 4 |  | .04
7 | 5 | .05 | 17 |  | 11 |  | .11
8 | 3 | .03 | 18 |  | 3 |  | .03
9 | 3 | .03 | 19 |  | 0 |  | .00
10 | 2 | .02 | 20 |  | 4 |  | .04
 |  |  |  |  | 80 |  | 
Cannot have a negative percent defective

## Slide 41: p-Chart for Data Entry
.11 –
.10 –
.09 –
.08 –
.07 –
.06 –
.05 –
.04 –
.03 –
.02 –
.01 –
.00 –
Sample number
Fraction defective
| | | | | | | | | |
2 4 6 8 10 12 14 16 18 20
UCLp = 0.10
LCLp = 0.00
p = 0.04

## Slide 42: p-Chart for Data Entry
.11 –
.10 –
.09 –
.08 –
.07 –
.06 –
.05 –
.04 –
.03 –
.02 –
.01 –
.00 –
Sample number
Fraction defective
| | | | | | | | | |
2 4 6 8 10 12 14 16 18 20
UCLp = 0.10
LCLp = 0.00
p = 0.04
Possible assignable causes present

## Slide 43: p-Chart Example
Quality control/p-chart | 
Number of samples | 8
Sample size | 10
Data | 
 | # Defects
Sample 1 | 2
Sample 2 | 1
Sample 3 | 3
Sample 4 | 2
Sample 5 | 3
Sample 6 | 0
Sample 7 | 5
Sample 8 | 0

## Slide 44: C-Chart
# Defects

## Slide 45: c-Chart Example
Quality control/c-chart | 
Number of samples | 10
Data | 
 | # Defects
Sample 1 | 2
Sample 2 | 1
Sample 3 | 2
Sample 4 | 9
Sample 5 | 3
Sample 6 | 2
Sample 7 | 1
Sample 8 | 0
Sample 9 | 3
Sample 10 | 2
Cannot be a
negative number

## Slide 46: Which Control Chart to Use
Examples
Length
Width
Distance
TABLE S6.3 | Helping You Decide Which Control Chart to Use
VARIABLE DATA USING AN x-CHART AND R-CHART | 
Observations are variables Collect 20 – 25 samples of n = 4, or n = 5, or more, each from a stable process and compute the mean for the x-chart and range for the R-chart Track samples of n observations | 

## Slide 47: Which Control Chart to Use
TABLE S6.3 | Helping You Decide Which Control Chart to Use
ATTRIBUTE DATA USING A P-CHART | 
Observations are attributes that can be categorized and a total number determined We deal with fraction, proportion, or percent defectives There are several samples, with many observations in each | 
Examples
Cell phones that don’t work compared to those that do
Pages in a report that have errors compared to total pages in the report

## Slide 48: Which Control Chart to Use
TABLE S6.3 | Helping You Decide Which Control Chart to Use
ATTRIBUTE DATA USING A C-CHART | 
Observations are attributes whose defects per unit of output can be counted We deal with the number counted, which is a small part of the possible occurrences Defects may be: number of blemishes on a desk; flaws in a bolt of cloth; crimes in a year; broken seats in a stadium; typos in a chapter of this text; or complaints in a day | 
Examples
Cracks on a cell phone screen
Number of buttons that don’t work
Number of words per page that are wrong

## Slide 49: Process Capability
The natural variation of a process should be small enough to produce products that meet the standards required
A process in statistical control does not necessarily meet the design specifications
Process capability is a measure of the relationship between the natural variation of the process and the design specifications

## Slide 50: Process Capability
Tolerances
  Design specifications reflecting product requirements
Process capability
  Range of natural variability in a process what we measure with control charts

## Slide 51: SPC and Process Variability
(a) Acceptance sampling (Some bad units accepted; the "lot" is good or bad)
(b) Statistical process control (Keep the process "in control")
(c) Cpk > 1 (Design a process that is in within specification)
Lower specification limit
Upper specification limit
Process mean, m
Figure S6.10
Notes: This may be a good time to stress that an overall goal of statistical process control is to “do it better,” i.e., improve over time.

## Slide 52: Additional Info
To assist with homework

## Slide 53: Total Quality Management (TQM)
Encompasses entire organization from supplier to customer
Stresses a commitment by management to have a continuing companywide drive toward excellence in all aspects of products and services that are important to the customer

## Slide 54: Continuous Improvement
Never-ending process of continuous improvement
Covers people, equipment, suppliers, materials, procedures
Every operation can be improved

## Slide 55: Six Sigma
Originally developed by Motorola, adopted and enhanced by Honeywell and GE
Highly structured approach to process improvement
    A strategy
    A discipline – DMAIC
    A set of 7 tools

## Slide 56: Costs of Quality
External Failure
Total Cost
Internal Failure
Prevention
Appraisal
Total Cost
Quality Improvement

## Slide 57: Seven Tools of TQM
Hour
Defect 1 2 3 4 5 6 7 8
A
B
C
(1) Check Sheet: An organized method of recording data
Figure 6.6
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/

## Slide 58: Seven Tools of TQM
(2) Scatter Diagram: A graph of the value of one variable vs. another variable
Absenteeism
Productivity
Figure 6.6

## Slide 59: Causes of Low Quality
https://www.conceptdraw.com/samples/fishbone-diagram

## Slide 60: Fishbone Details
https://www.conceptdraw.com/samples/fishbone-diagram

## Slide 61: Seven Tools of TQM
(5) Flowchart (Process Diagram): A chart that describes the steps in a process
Figure 6.6

## Slide 62: Flow Charts
MRI Flowchart
Physician schedules MRI
Patient taken to MRI
Patient signs in
Patient is prepped
Technician carries out MRI
Technician inspects film
If unsatisfactory, repeat
Patient taken back to room
MRI read by radiologist
MRI report transferred to physician
Patient and physician discuss
11
10
20%
9
8
80%
1
2
3
4
5
6
7

## Slide 63: Seven Tools of TQM
(6) Histogram: A distribution showing the frequency of occurrences of a variable
Figure 6.6
Distribution
Repair time (minutes)
Frequency

## Slide 64: Statistical Process Control (SPC)

## Slide 65: SPC Outline
Basics of Statistical Process Control
Control Charts
Control Charts for Attributes
Control Charts for Variables
SPC with Excel
Process Capability

## Slide 66: SPC in TQM
SPC
  Tool for identifying problems and make improvements
  Contributes to the TQM goal of continuous improvements

## Slide 67: Statistical Process Control (SPC)
The objective of a process control system is to provide a statistical signal when assignable causes of variation are present

## Slide 68: Statistical Process Control (SPC)
Uses statistics and control charts to tell when to take corrective action
Drives process improvement
Four key steps
  Measure the process
  When a change is indicated, find the assignable cause
  Eliminate or incorporate the cause
  Restart the revised process

## Slide 69: SPC Sampling
To measure the process, we take samples and analyze the sample statistics following these steps
(a) Samples of the product, say five boxes of cereal taken off the filling machine line, vary from each other in weight
Frequency
Weight
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
#
Each rectangle represents one sample of five boxes of cereal
Figure S6.1

## Slide 70: SPC Sampling
To measure the process, we take samples and analyze the sample statistics following these steps
(b) After enough samples are taken from a stable process, they form a pattern called a distribution
The solid line represents the distribution
Frequency
Weight
Figure S6.1

## Slide 71: SPC Sampling
(c) There are many types of distributions, including the normal (bell-shaped) distribution, but distributions do differ in terms of central tendency (mean), standard deviation or variance, and shape
Weight
Central tendency
Weight
Variation
Weight
Shape
Frequency
Figure S6.1
To measure the process, we take samples and analyze the sample statistics following these steps

## Slide 72: SPC Sampling
To measure the process, we take samples and analyze the sample statistics following these steps
(d) If only natural causes of variation are present, the output of a process forms a distribution that is stable over time and is predictable
Weight
Time
Frequency
Prediction
Figure S6.1

## Slide 73: SPC Sampling
To measure the process, we take samples and analyze the sample statistics following these steps
(e) If assignable causes are present, the process output is not stable over time and is not predicable
Weight
Time
Frequency
Prediction
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Figure S6.1

## Slide 74: Sample Quality Control Chart

## Slide 75: Process Control Chart
1
2
3
4
5
6
7
8
9
10
Sample number
Upper
control
limit
Process
average
Lower
control
limit
Out of control

## Slide 76: x- bar Chart Example (cont.)
UCL = 5.08
LCL = 4.94
Mean
Sample number
|
1
|
2
|
3
|
4
|
5
|
6
|
7
|
8
|
9
|
10
5.10 –
5.08 –
5.06 –
5.04 –
5.02 –
5.00 –
4.98 –
4.96 –
4.94 –
4.92 –
x = 5.01
=

## Slide 77: R-Chart Example (cont.)
UCL = 0.243
LCL = 0
Range
Sample number
R = 0.115
|
1
|
2
|
3
|
4
|
5
|
6
|
7
|
8
|
9
|
10
0.28 –
0.24 –
0.20 –
0.16 –
0.12 –
0.08 –
0.04 –
0 –

## Slide 78: p-Chart Example (cont.)
0.02
0.04
0.06
0.08
0.10
0.12
0.14
0.16
0.18
0.20
Proportion defective
Sample number
2
4
6
8
10
12
14
16
18
20
UCL = 0.190
LCL = 0.010
p = 0.10

## Slide 79: c-Chart (cont.)
3
6
9
12
15
18
21
24
Number of defects
Sample number
2
4
6
8
10
12
14
16
UCL = 23.35
LCL = 1.99
c = 12.67

## Slide 80: Process Capability
(b) Design specifications and natural variation the same; process is capable of meeting specifications most of the time.
Design Specifications
Process
(a) Natural variation exceeds design specifications; process is not capable of meeting specifications all the time.
Design Specifications
Process

## Slide 81: Process Capability (cont.)
(c) Design specifications greater than natural variation; process is capable of always conforming to specifications.
Design Specifications
Process
(d) Specifications greater than natural variation, but process off center; capable but some output will not meet upper specification.
Design Specifications
Process