## Slide 1
Process Strategy
7

## Slide 2: Process Strategy
The objective is to create a process to produce offerings that meet customer requirements within cost and other managerial constraints

## Slide 3: Process Strategies
How to produce a product or provide a service that
  Meets or exceeds customer requirements
  Meets cost and managerial goals
Has long-term effects on
  Efficiency and production flexibility
  Costs and quality

## Slide 4: Process Planning
Make-or-buy decisions
Process selection
Specific equipment selection
Process plans
Process analysis

## Slide 5: Make-or Buy Example
Assume you can lease an item you need for a project for $150/day. To purchase the item, the investment cost is $1,000, and the daily cost would be another $50/day.
  If you need the item for 12 days, should you lease it or purchase it?
  How long will it take for the lease cost to be the same as the purchase cost?
Use Excel template

## Slide 6: Make-or Buy Solution
Set up an equation so the “make” is equal to the “buy”
In this example, use the following equation. Let d be the number of days to use the item.
  $150d = $1,000 + $50d
Solve for d as follows:
  Subtract $50d from the right side of the equation to get
  $100d = $1,000
  Divide both sides of the equation by $100
  d = 10 days
The lease cost is the same as the purchase cost at 10 days
If you need the item for 12 days, it would be more economical to purchase it
USE EXCEL TEMPLATE

## Slide 7: Make vs Buy
See spreadsheet
A firm's must decide whether to make or buy 18,000 items used in their production line.
  The costs for making the item are $98,000 annual cost and a $40 cost per item.
  The costs for buying the item are $45 per item.
  Should the company make or buy this item?

## Slide 8: Crossover/Cost-Volume Analysis
Borges Machine​ Shop, Inc., has a​ 1-year contract for the production of 200,000 gear housings for a new​ off-road vehicle. Owner Luis Borges hopes the contract will be extended and the volume increased next year. Borges has developed costs for three alternatives. They are​ general-purpose equipment ​(GPE), flexible manufacturing system​ (FMS), and​ expensive, but​ efficient, dedicated machine​ (DM).
The cost data​ are given in the table below
  The option GPE is best when the contracted volume is below 37,500 units ​(enter your response as a whole​ number).
  The option FMS is best when the contracted volume is between 37,500 and 300,000 units ​(enter your responses as whole​ numbers).
  The option DM is best when the contracted volume is over 300,000 units ​(enter your response as a whole​ number).

## Slide 9: Process Strategies
Four basic strategies
  Process focus
  Repetitive focus
  Product focus
  Mass customization
Within these basic strategies there are many ways they may be implemented

## Slide 10: Process, Volume, and Variety
Process Focus
projects, job shops (machine, print, hospitals, restaurants)
Arnold Palmer Hospital
Repetitive
(autos, motorcycles, home appliances)
Harley-Davidson
Product Focus
(commercial baked goods, steel, glass, beer)
Frito-Lay
High Variety
one or few units per run,
(allows customization)
Changes in Modules
modest runs, standardized modules
Changes in Attributes (such as grade, quality, size, thickness, etc.)
high throughput and/or long runs only
Mass Customization
(difficult to achieve, but huge rewards)
Dell Computer
Poor Strategy (Both fixed and variable costs are high)
Low Volume
Repetitive Process
High Volume
Volume
Figure 7.1
Variety (flexibility)

## Slide 11: Process Focus
Many inputs
(surgeries, sick patients, baby deliveries, emergencies)
Many different outputs (uniquely treated patients)
Many departments and many routings
Figure 7.2(a)
(low-volume, high-variety, intermittent processes)
Arnold Palmer Hospital

## Slide 12: Repetitive Focus
Raw materials and module inputs
Modules combined for many
Output options
(many combinations of motorcycles)
Few modules
(multiple engine models, wheel modules)
Figure 7.2(b)
(modular)
Harley Davidson

## Slide 13: Product Focus
Few inputs
(corn, potatoes, water, seasoning)
Output variations in size, shape, and packaging
(3-oz, 5-oz, 24-oz package labeled for each material)
Figure 7.2(c)
(high-volume, low-variety, continuous process)
Frito-Lay

## Slide 14: Mass Customization
Figure 7.2(b)
(high-volume, high-variety)
Dell Computer
Many parts and component inputs
Many output versions
(custom PCs and notebooks)
(chips, hard drives, software, cases)
Many modules

## Slide 15: Mass Customization
TABLE 7.1 | Mass Customization Provides More Choices Than Ever |  | 
 |  | NUMBER OF CHOICES | 
ITEM |  | 1970s | 21ST CENTURY
Vehicle styles |  | 18 | 1,212
Bicycle types |  | 8 | 211,000
iPhone mobile game apps |  | 0 | 1,200,000
Web sites |  | 0 | 634,000,000
Movie releases per year |  | 267 | 1551
New book titles |  | 40,530 | 300,000+
Houston TV channels |  | 5 | 185
Breakfast cereals |  | 160 | 340
Items (SKUs) in supermarkets |  | 14,000 | 150,000
High-definition TVs |  | 0 | 102

## Slide 16: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Small quantity and large variety of products |  | Long runs, a standardized product from modules | Large quantity and small variety of products | Large quantity and large variety of products
Broadly skilled operators |  | Moderately trained employees | Less broadly skilled operators | Flexible operators

## Slide 17: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Instructions for each job |  | Few changes in the instructions | Standardized job instructions | Custom orders requiring many job instructions
High inventory |  | Low inventory | Low inventory | Low inventory relative to the value of the product

## Slide 18: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Finished goods are made to order and not stored |  | Finished goods are made to frequent forecasts | Finished goods are made to a forecast and stored | Finished goods are build-to-order (BTO)
Scheduling is complex |  | Scheduling is routine | Scheduling is routine | Sophisticated scheduling accommodates custom orders

## Slide 19: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Fixed costs are low and variable costs high |  | Fixed costs are dependent on flexibility of the facility | Fixed costs are high and variable costs low | Fixed costs tend to be high and variable costs low

## Slide 20: Production Technology
Machine technology
Automatic identification systems (AISs)
Process control
Vision systems
Robots
Automated storage and retrieval systems (ASRSs)
Automated guided vehicles (AGVs)
Flexible manufacturing systems (FMSs)
Computer-integrated manufacturing (CIM)

## Slide 21: Process Analysis and Design
Flowchart
  Shows the movement of materials
  Harley-Davidson flowchart
Time-Function Mapping
  Shows flows and time frame

## Slide 22: "Baseline" Time-Function Map
Customer
Sales
Production control
Plant A
Warehouse
Plant B
Transport
12 days
13 days
1 day
4 days
1 day
10 days
1 day
9 day
1 day
52 days
Figure 7.4(a)
Move
Receive product
Product
Product
Extrude
Wait
WIP
Product
Move
Wait
WIP
WIP
Print
Wait
Order
WIP
Order product
Process order
Wait
Order

## Slide 23: "Target" Time-Function Map
Customer
Sales
Production control
Plant
Warehouse
Transport
1 day
2 days
1 day
1 day
1 day
6 days
Figure 7.4(b)
Move
Receive product
Product
Product
Extrude
Wait
Print
Order
WIP
Product
Order product
Process order
Wait
Order

## Slide 24: Burger Process for Chef
Text
Text
Text
Text
Text
Text
Text
Text
Text
Text
Text
Figure 7.5
Text
Text
Text
Text
Text
Text
Text
Text
Text
Assemble your process flow chart below.

## Slide 25: Burger Process – SOLUTION
Figure 7.5
Broiler
Transfer to broiler
Visual inspection
Patty In Storage
Transfer to rack
Temporary storage
Obtain buns, lettuce, etc…
Assemble order
Place in finish rack

## Slide 26: Service Blueprinting
Focuses on the customer and provider interaction
Defines three levels of interaction
Each level has different management issues
Identifies potential failure points

## Slide 27: Service Blueprint
Personal Greeting
Service Diagnosis
Perform Service
Friendly Close
Level
#3
Level
#1
Level
#2
Figure 7.7
No
Notify customer and recommend an alternative provider.
(7 min)
Customer arrives for service.
(3 min)
Warm greeting and obtain service request.
(10 sec)
F
Direct customer to waiting room.
F
Notify customer the car is ready.
(3 min)
Customer departs
Customer pays bill.
(4 min)
F
F
Perform required work.
(varies)
Prepare invoice.
(3 min)
F
F
Yes
F
Yes
F
Standard request.
(3 min)
Determine specifics.
(5 min)
No
Can service be done and does customer approve?
(5 min)

## Slide 28: Process Redesign
The fundamental rethinking of business processes to bring about dramatic improvements in performance
Relies on reevaluating the purpose of the process and questioning both the purpose and the underlying assumptions
Requires reexamination of the basic process and its objectives
Focuses on activities that cross functional lines
Any process is a candidate for redesign

## Slide 29: Process Analysis and Design
Value-Stream Mapping (VSM)
  Where value is added in the entire production process, including the supply chain
  Extends from the customer back to the suppliers

## Slide 30: Value-Stream Mapping
Begin with symbols for customer, supplier, and production to ensure the big picture
Enter customer order requirements
Calculate the daily production requirements
Enter the outbound shipping requirements and delivery frequency
Determine inbound shipping method and delivery frequency
Add the process steps (i.e., machine, assemble) in sequence, left to right
Add communication methods, add their frequency, and show the direction with arrows
Add inventory quantities between every step of the entire flow
Determine total working time (value-added time) and delay (non-value-added time)

## Slide 31: Value-Stream Mapping
Figure 7.6