## Slide 1
Waiting-Line Models
D
MODULE
NOTE: Queue = Waiting Line

## Slide 2: Outline
Queuing Theory
Characteristics of a Waiting-Line System
Queuing Costs
The Variety of Queuing Models
Other Queuing Approaches

## Slide 3: Queuing Theory
The study of waiting lines
Waiting lines are common situations
Occur in
  Manufacturing
  Service
This is a customer facing operation
  Product many times judged based on waiting

## Slide 4: Common Queuing Situations
TABLE D.1 | Common Queuing Situations |  | 
SITUATION |  | ARRIVALS IN QUEUE | SERVICE PROCESS
Supermarket |  | Grocery shoppers | Checkout clerks at cash register
Highway toll booth |  | Automobiles | Collection of tolls at booth
Doctor’s office |  | Patients | Treatment by doctors and nurses
Computer system |  | Programs to be run | Computer processes jobs
Telephone company |  | Callers | Switching equipment forwards calls
Bank |  | Customer | Transactions handled by teller
Machine maintenance |  | Broken machines | Repair people fix machines
Harbor |  | Ships and barges | Dock workers load and unload

## Slide 5: Parts of a Waiting Line
Figure D.1
Dave’s
Car Wash
Enter
Exit
Population of
dirty cars
Arrivals
from the
general
population …
Queue
(waiting line)
Service
facility
Exit the system
Arrivals to the system
Exit the system
In the system

## Slide 6: Arrival Characteristics
Size of the arrival population
  Unlimited (infinite) or limited (finite)
Pattern of arrivals
  Scheduled or random, often a Poisson distribution
    Constant and known rate independent of other events
Behavior of arrivals
  Wait in the queue and do not switch lines
  No balking or reneging

## Slide 7: Waiting-Line Characteristics
Queue length
  Limited or unlimited
Queue discipline
  First-in, first-out (FIFO) is most common
Priority rules
  For example: Hospitals us a triage system

## Slide 8: Service Characteristics
Queuing system designs
  Single-server system, multiple-server system
  Single-phase system, multiphase system
Service time distribution
  Constant service time
  Random service times
Statistical distribution of service
  Service rate
    Where, when, and how much
Service costs

## Slide 9: Queuing System Designs
Figure D.3
Departures
after service
Single-server, single-phase system
Queue
Arrivals
Single-server, multiphase system
Arrivals
Departures
after service
Phase 1 service facility
Phase 2 service facility
Service facility
Queue
A family dentist's office
A fast-food, dual-window drive-through

## Slide 10: Queuing System Designs
Figure D.3
Multi-server, single-phase system – One channel handles all actions
Arrivals
Queue
Most bank and post office service windows
Departures
after service
Service facility
Channel 1
Service facility
Channel 2
Service facility
Channel 3

## Slide 11: Queuing System Designs
Figure D.3
Multi-server, multiphase system – Different phases can specialize
Arrivals
Queue
Some college cafeterias
Departures
after service
Phase 2 service facility
Channel 1
Phase 2 service facility
Channel 2
Phase 1 service facility
Channel 1
Phase 1 service facility
Channel 2

## Slide 12: Other Queuing Approaches
The single-phase models cover many queuing situations
Variations of the four single-phase systems are possible
Multiphase models exist for more complex situations

## Slide 13: Queue Performance Variables
Arrival rate ()
Service rate ()
Number of servers
Server cost ($/time)
Waiting cost ($/time)
  Based on lost customers who balk or renege
Average server utilization ()
Average queue length/number (Lq)
Average system length/number (Ls)
Average time in queue (Wq)
Average time in system (Ws)
Probability service facility will be idle (P0)%
Cost of waiting
Cost of system
Probability of a specific number of customers in the system
= Probability of more than k units in the system, where n is the number of units in the system
Calculated using ExcelOM
Pn>k =

## Slide 14: Queuing Costs
Figure D.5
Total expected cost
Cost of providing service
Cost
Low level
of service
High level
of service
Cost of waiting time
Minimum
Total
cost
Optimal
service level

## Slide 15: Queuing Models
The four queuing models that follow all assume:
  Poisson distribution arrivals
  FIFO discipline
  A single-service phase

## Slide 16: Queuing Models
MODEL | NAME | EXAMPLE | NUMBER OF SERVERS (CHANNELS) | NUMBER OF PHASES | ARRIVAL RATE PATTERN | SERVICE TIME PATTERN | POPULATION SIZE
A | Single-server system (M/M/1) | Information counter at department store | Single | Single | Poisson | Negative exponential | Unlimited
B | Multiple-server (M/M/S) | Airline ticket counter | Multi-server | Single | Poisson | Negative exponential | Unlimited
C | Constant-service (M/D/1) | Automated car wash | Single | Single | Poisson | Constant | Unlimited
D | Finite population (M/M/1 with finite source) | Shop with only a dozen machines that might break | Single | Single | Poisson | Negative exponential | Limited
All assume FIFO

## Slide 17: Types of Queues
What type of queuing model might be used for the following examples?
  Wal-Mart checkout
  Environmental consulting company
  Car assembly line
  Doctor’s office – No emergencies
  Doctor’s office – with emergencies
  Traffic jam
  A photographer taking individual pictures for a sports team

## Slide 18: Types of Queues
What type of queuing model might be used for the following examples?
  Wal-Mart checkout: A or B
  Environmental consulting company: B
  Car assembly line: C
  Doctor’s office – No emergencies: A
  Doctor’s office – With emergencies: B
  Traffic jam: A, B, or C
  A photographer taking individual pictures for a sports team: D

## Slide 19: Model A – Single-Server
Arrivals are served on a FIFO basis
  Every arrival waits to be served regardless of the length of the queue
Arrivals are independent of preceding arrivals
Average number of arrivals does not change over time
Arrivals are described by a Poisson probability distribution
Come from an infinite population
Service times vary from one customer to the next and are independent of one another
  But average rate is known
Service times occur according to the negative exponential distribution
The service rate is faster than the arrival rate

## Slide 20: Model A – Single-Server
TABLE D.3 |  | Queuing Information for Model A: Single-Server System, M/M/1
λ | = average number of arrivals per time period | 
μ | = average number of people or items served per time period (average service rate) | 
Ls | = average number of units (customers) in the system (waiting and being served) | 
Ws | = average time a unit spends in the system (waiting time plus service time) | 
Lq | = average number of units waiting in the queue
Wq | = average time a unit spends waiting in the queue
Ρ | = utilization factor for the system:
P0 | = Probability of 0 units in the system (that is, the service unit is idle) | 
Pn>k | = probability of more than k units in the system, where n is the number of units in the system | 
NOTE: For reference, equations can be found in the book

## Slide 21: Single-Server Example
A car mechanic has the following data:
 = 2 cars arriving/hour; µ= 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?

## Slide 22: Single-Server Example
A car mechanic has the following data:
 = 2 cars arriving/hour; µ= 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?

## Slide 23: Single-Server Example (cont)
A car mechanic has the following data:
 = 2 cars arriving/hour; µ= 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?
What is the average time to wait in the queue?
What is the probability the mechanic is busy?
What is the probability there are no cars waiting or being serviced?

## Slide 24: Single-Server Example (cont)
A car mechanic has the following data:
 = 2 cars arriving/hour; µ= 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?
What is the average time to wait in the queue?
What is the probability the mechanic is busy?
What is the probability there are no cars waiting or being serviced?
P0 = 33% probability there are 0 cars in the system
Wq = 2/3 hour = 40 minute average waiting time
 = 67% of time mechanic is busy

## Slide 25: Single-Server Example Cost
The car mechanic has estimated the following cost data:
Customer dissatisfaction and lost goodwill = $15 per hr
Mechanic's salary = $88 per day
What is the cost, per day, to the mechanic for people to wait in the queue?
What is the total cost, per day, including servicing?

## Slide 26: Single-Server Example Cost
The car mechanic has estimated the following cost data:
Customer dissatisfaction and lost goodwill = $15 per hr
Mechanic's salary = $88 per day
What is the cost, per day, to the mechanic for people to wait in the queue?
What is the total cost, per day, including servicing?
Total expected waiting costs = $248 per day
Total system costs = $328 per day

## Slide 27: Multiple-Server Model
TABLE D.4
Additional Queuing Information for Model B: Multiple-Server System, also Called M/M/S
M = number of servers (channels) open

## Slide 28: Multiple-Server Example
The car mechanic has the same data as before; however, the shop now has 2 mechanics.
 = 2 cars arriving/hour; µ = 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?

## Slide 29: Multiple-Server Example
The car mechanic has the same data as before; however, the shop now has 2 mechanics.
 = 2 cars arriving/hour; µ = 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?

## Slide 30: Multiple-Server Example (cont)
The car mechanic has the same data as before; however, the shop now has 2 mechanics.
 = 2 cars arriving/hour µ = 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?
What is the average time to wait in the queue?
What is the probability the mechanic is busy?
What is the probability there are no cars waiting or being serviced?

## Slide 31: Multiple-Server Example (cont)
The car mechanic has the same data as before; however, the shop now has 2 mechanics.
 = 2 cars arriving/hour µ = 3 cars serviced/hour
What is the average number of cars in the system?
What is the average wait time?
What is the average number of cars waiting in the queue?
What is the average time to wait in the queue?
What is the probability the mechanic is busy?
What is the probability there are no cars waiting or being serviced?
Wq = 0.04x60 = 2.5 minute average waiting time
 = 33% of time mechanic is busy
P0 = 50% probability there are 0 cars in the system

## Slide 32: Multiple-Server Example Cost
The car mechanic has estimated the following cost data:
Customer dissatisfaction and lost goodwill = $15 per hr
Mechanic's salary = $88 per day
What is the cost, per day, to the mechanic for people to wait in the queue?
What is the total cost, per day, including servicing?

## Slide 33: Multiple-Server Example Cost
The car mechanic has estimated the following cost data:
Customer dissatisfaction and lost goodwill = $15 per hr
Mechanic's salary = $88 per day
What is the cost, per day, to the mechanic for people to wait in the queue?
What is the total cost, per day, including servicing?
Total expected waiting costs = $186 per day
Total system costs = $266 per day

## Slide 34: Examples Comparison
Metric | One Mechanic | Two Mechanics
Server Utilization () | 67% | 33%
System Empty (P0) | 33% | 50%
Length Queue (Lq) | 1.33 cars | 0.08 cars
Length system (Ls) | 2.00 cars | 0.75 cars
Time Queue (Wq) | 40 minutes | 3 minutes
Time System (Ws) | 60 minutes | 23 minutes
Cost Waiting | $248 | $186
Cost System | $328 | $266
Which model is better?

## Slide 35: Waiting-Line Table Example
A bank has the following queuing information for how fast bank tellers process customers
= 18, µ = 20
Calculate the queue time for 1, 2, 3, and 4 tellers

## Slide 36: Waiting-Line Table Example
A bank has the following queuing information for how fast bank tellers process customers
= 18, µ = 20
Calculate the queue time for 1, 2, 3, and 4 tellers
NUMBER OF SERVERS | M | NUMBER IN QUEUE | TIME IN QUEUE
1 window | 1 | 8.100 | .45 hrs, 27 minutes
2 windows | 2 | 0.229 | .0127 hrs, 46 seconds
3 windows | 3 | 0.030 | .0017 hrs, 6 seconds
4 windows | 4 | 0.004 | .0002 hrs, <1 second

## Slide 37: Constant-Service-Time Example
Trucks currently wait 15 minutes on average
Truck and driver cost $60 per hour
Automated compactor service rate (µ) = 12 trucks per hour
Arrival rate () = 8 per hour
Compactor costs $3 per truck
Complete the table below.
 | Constant Service
P0 | 
Ls | 
Ws | 
Lq | 
Wq | 
System Cost | 

## Slide 38: Constant-Service-Time Example
Trucks currently wait 15 minutes on average
Truck and driver cost $60 per hour
Automated compactor service rate (µ) = 12 trucks per hour
Arrival rate () = 8 per hour
Compactor costs $3 per truck
Complete the table below.
Current waiting cost per trip = (1/4 hr)($60) = $15 /trip
 | Constant Service
P0 | 33%
Ls | 1.33
Ws | 10.0 min
Lq | 0.67
Wq | 5.0 min
System Cost | $23.00

## Slide 39: Finite-Population Model
Assumptions
  There is only one server
  The population of units seeking service is finite
  Arrivals follow a Poisson distribution
  Customers are served on a first-come, first-served basis

## Slide 40: Finite-Population Example
Laser printer breakdown analysis
# = 5, l = 0.05 printers/hour, m = 0.50 printers/hour
Complete the data below.
P0 =
Lq =
Ls =
Wq =
Ws =

## Slide 41: Finite-Population Example
P0 = 56%
Lq = 0.2 printers
Ls = 0.64 printers
Wq = 0.93 hours
Ws = 2.93 hours
Laser printer breakdown analysis
# = 5, l = 0.05 printers/hour, m = 0.50 printers/hour
Complete the data below.

## Slide 42: Finite-Population Example
For the previous situation, the company wants to know how much the printer servicing is costing the company per hour.
Ls = 0.64 printers
Alternative printing methods cost per hour = $120
Technician cost per hour = $25
Hourly cost computed as below:
(Units in system)(Downtime cost) + Service cost
Hourly cost = (Average number of printers down)(Cost per downtime hour) + Cost per technician hour
= (0.64)($120) + $25
= $76.80 + $25.00
= $101.80 per hour

## Slide 43: Advanced Problem
Use data below to determine how many sales people the company should hire.
Average of 60 customers per shift
Average waiting times
  One salesperson = 14 minutes
  Two salespeople = 8 minutes
  Three salespeople = 4 minutes
  Four salespeople = 3 minutes
Cost per minute that customers wait at ​$1.25
Cost per salesperson per shift​ (including fringe​ benefits) is ​$95
One​ Server: Total cost per shift​ = $___
Two​ Servers: Total cost per shift​ = $___
Three​ Servers: Total cost per shift​ = $___
Four​ Servers: Total cost per shift​ = $___
Hire _ salespeople.

## Slide 44: Advanced Problem
Use data below to determine how many sales people the company should hire.
Average of 60 customers per shift
Average waiting times
  One salesperson = 14 minutes
  Two salespeople = 8 minutes
  Three salespeople = 4 minutes
  Four salespeople = 3 minutes
Cost per minute that customers wait at ​$1.25
Cost per salesperson per shift​ (including fringe​ benefits) is ​$95
One​ Server: Total cost per shift​ = $1,145
Two​ Servers: Total cost per shift​ = $790
Three​ Servers: Total cost per shift​ = $585
Four​ Servers: Total cost per shift​ = $605
Hire 3 salespeople.